## Slide 1
Production test flow — yield and quantity
2026-W33 · 2026-08-10 to 2026-08-16, week still running · UTC · first-pass yield, units in the box
ASIC @Sigurd
WST
35.3% reported
FT
84.3% reported
SLT
at Sigurd
PCBA L6 @Pega
SMT / ICT
ASSY
MLT
65.5% 228 units
HTT
54.3% 170 units
FATP L10 2U/4U
ASSY
4U / 2U
FATP L10 6U
ASSY
2U
3 units too few for a yield
FAT
2 units too few for a yield
SFT
1 units too few for a yield
Runin
1 units too few for a yield
Rack L11
ASSY
Provisioning
SFT / Runin
2 units too few for a yield
Pack
Green = the step yields and we measure it. Amber = it ran, under 20 units, so no yield is reported — the count is. Grey = builds or moves, no verdict.
Source: pega2 – pega5 (ESVM), one row per unit. WST and FT reported by Sigurd. VBB provisioning omitted — not part of the product test flow. Amber this week: L10 FAT (2u), L10 SFT (1u), L10 RIN (1u), L10 2U (3u), L11 Test (2u).

## Slide 2
Every step, with the retest rate
2026-W33 · retest rate is the share of units that had to be run again
Test step
Units
Runs
First pass
After retest
Retest rate
Top failure
WST reported
35.3%
Sigurd, as of 2026-08-14
FT reported
84.3%
Sigurd, as of 2026-08-14
MLT pega3
228
279
65.5%
74.6%
19.7%
45 of 228 units re-run
SohuPowerVirusTestCase
HTT pega3
170
234
54.3%
68.8%
27.6%
47 of 170 units re-run
SohuRdqsSweepTrainingTestCase
L10 FAT pega4
2
15
not enough units
—
100.0%
2 of 2 units re-run
SohuHostRebootTestCase
L10 SFT pega4
1
6
not enough units
—
100.0%
1 of 1 units re-run
SohuLlama70bHp8ForwardIteratedTestCase
L10 RIN pega4
1
4
not enough units
—
100.0%
1 of 1 units re-run
RunInStress
L10 2U pega4
3
19
not enough units
—
66.7%
2 of 3 units re-run
BmcCheck
L11 Test pega5
2
16
not enough units
—
100.0%
2 of 2 units re-run
CheckSohuServerNoErrorLogTestCase
Rolled first-pass across MLT × HTT: 35.6%
Steps under 20 first-time units report counts only. Full unit-level source data, every serial and release with a link to its run: 32x-production.i.etched.com/week.html#week=2026-W33