## Slide 1
End-to-end first-pass yield, by test step
2026-08-09 → 2026-08-15 (UTC) · production test engineering
Rolled first-pass, board stages
28.1%
VBB Provisioning × MLT × HTT
Die to module, incl. Sigurd
8.4%
WST 35.3% × FT 84.3% × board stages
Measured this week
432
units · 641 runs · 8 stages
The line loses most of its yield at module test. MLT first-pass 65.5% and HTT 54.3%. Retest recovers them to 74.6% and 68.8%, which is why the run-level pass rate looks better than the line feels.
Downstream is bring-up, not production. L10 and L11 ran 9 units all week between them — below the threshold where a yield can be read at all, so they are excluded from the rolled figure rather than dragging it to zero.
Two of the five upstream numbers are hand-carried. WST and FT come from Sigurd by message, not by pipeline.

## Slide 2
Every step, seven days
first pass · after retest · retest load
Test step
Units
Runs
First pass
After retest
Retest load
Top failure
WST reported
—
—
35.3%
—
—
Sigurd, as of 2026-08-14
FT reported
—
—
84.3%
—
—
Sigurd, as of 2026-08-14
VBB Provisioning pega2
25
68
79.2%
100.0%
—
LcusDisable
MLT pega3
228
279
65.5%
74.6%
19.7%
SohuPowerVirusTestCase
HTT pega3
170
234
54.3%
68.8%
27.6%
SohuRdqsSweepTrainingTestCase
L10 FAT pega4
2
15
0.0%
50.0%
100.0%
SohuHostRebootTestCase
L10 SFT pega4
1
6
—
0.0%
100.0%
SohuLlama70bHp8ForwardIteratedTestCase
L10 RIN pega4
1
4
100.0%
100.0%
100.0%
RunInStress
L10 2U pega4
3
19
0.0%
33.3%
66.7%
BmcCheck
L11 Test pega5
2
16
0.0%
50.0%
100.0%
CheckSohuServerNoErrorLogTestCase
Greyed rows ran fewer than 20 first-time units this week — too few to read a yield from.

## Slide 3
Where MLT and HTT lose units
failure signatures, seven days, containers excluded
MLT first pass 65.5% · after retest 74.6% · 45 of 228 units retested
SohuPowerVirusTestCase ×140 Power Virus / Thermal
C2cLinkupTestCase ×125 C2C
SohuPmbistTestCase ×100 PMBIST
SohuSaScreeningTestCase ×93 Other
SohuLlamaMttTestCase ×90 Llama / SaSort
HTT first pass 54.3% · after retest 68.8% · 47 of 170 units retested
SohuRdqsSweepTrainingTestCase ×49 RDQS Training
SohuLlamaForwardIteratedTestCase ×46 Llama / SaSort
SohuLlamaInferenceMaxTestCase ×44 Llama / SaSort
CheckFirmwareVersionTestCase ×17 Other
SetPllGlitchFreqTestCase ×17 Other
Retest load is the number to act on. 45 of 228 MLT units and 47 of 170 HTT units came back for a second run this week. Each one is a second occupancy of the stations that are already the line's constraint — the recovery to 74.6% and 68.8% is bought with station time, not won for free.

## Slide 4
Manufacturing readiness
what the seven days say about shipping
Module test is the constraint, and it is measurable. MLT and HTT carry 398 of the week's 432 units. Both are instrumented per unit, per slot, per failing test case — the failure Pareto above is queryable, not anecdotal.
L10 and L11 are not yet producing a signal. L10 FAT 2u, L10 SFT 1u, L10 RIN 1u, L10 2U 3u, L11 Test 2u across four stages in seven days. Before anyone reads a yield off these, they need volume; the honest status is bring-up.
Yield recovery is real but it is paid for in station time. The gap between first-pass and after-retest is 9 points at MLT and 15 at HTT. That gap is capacity spent twice.
The upstream half of the flow is still a manual handoff. WST 35.3% and FT 84.3% arrive by Slack message. Joining Sigurd's die-level data to our module-level data needs one field — a chip serial on our rows. pega3 returns asic_lot_code and it is empty on every run.

## Slide 5
Data sources and definitions
so every number here can be re-derived
First-pass yield — units whose first ever run at that step passed, over units seeing that step for the first time in the window. Attempts are numbered over 30 days of history, so a unit returning this week counts as a retest, not a fresh pass.
After retest — units that passed at least once in the window, over all units tested in it.
Retest load — units that needed more than one run in the window. Not reported for VBB provisioning, where the eight repeat runs are a provisioning sequence rather than second attempts.
Rolled first-pass — the product of the first-pass yields of the stages named on it. Stages with fewer than 20 first-time units are excluded, because a 0% on one unit would report the line at zero.
MLT / HTT / L10 / L11 — read directly from the station controllers (pega2–pega5), one row per unit rather than one per fixture. This is the same source the daily tracker is rebuilt from, and it does not match OCP Logs — the discrepancy is documented on the station page.
WST / FT — reported by Sigurd in #production-test-eng, as of 2026-08-14. Hand-entered here; not collected by this pipeline.
Built 2026-08-15 21:05:44 UTC from a1ce804 · live page: 32x-production.i.etched.com/fpy.html