## Slide 1
Basic Level of Production Metrics
2026-W36 · the three numbers this deck reports, and what each one is for
1. Capacity
How many units we are producing
171 units through 4 steps this week, across 221 runs.
It sets the schedule: a station cannot ship what it cannot test.
2. Yield
How many percentage we can ship vs total production
First pass 40.0% at MLT and 78.9% at HTT — — rolled across the two.
It sets how many units must be started to ship one.
3. Retest
How stable is the test
16.7% of MLT units and 11.9% of HTT units had to be run again — 15 and 8 units.
It is where yield loss turns into lost capacity.
Why it is broken out by test step: a line ships at the rate of its worst step, not its average — so the only useful version of these three numbers is one per step, in the order a unit travels.

## Slide 2
Production test flow — yield and quantity
2026-W36 · 2026-08-31 to 2026-09-06, week still running · UTC · first-pass yield and units, under each step
32.5% reported
— reported
at Sigurd — not collected here
90 units few units
67 units few units
VBB — outside the yield view
counted with FAT / SFT
L6 combined (MLT × HTT)
—
MLT 40.0% · HTT 78.9%
a module's chance of clearing both first time
Through the line
171 units
221 runs across 4 steps
Reading the numbers
A percentage is a first-pass yield: units that passed at their first attempt that week.
A count means no yield is reported. None are chassis and rack level and in bring-up — a percentage over three units swings 33 points on one of them.
Too few units this week: TIM, MLT, HTT, L11 Provision. WST and FT are reported by Sigurd. VBB is drawn for the flow and left out of the yield view.
Source: pega2, pega6, pega3, pega4, pega5 (ESVM), one row per unit.

## Slide 3
Every step, with the retest rate
2026-W36 · retest rate is the share of units that had to be run again
Test step
Units
Runs
First pass
After retest
Retest rate
Top failure
WST reported
32.5%
Sigurd, as of 2026-08-21
FT reported
—
Sigurd, as of 2026-08-14
TIM pega6
11
11
not enough units
90.9%
0.0%
0 of 11 units re-run
validate_coldplate_temperature
MLT pega3
90
106
not enough units
63.3%
16.7%
15 of 90 units re-run
SohuPmbistTestCase
HTT pega3
67
75
not enough units
85.1%
11.9%
8 of 67 units re-run
SohuLlamaForwardIteratedTestCase
L11 Provision pega5
3
29
not enough units
100.0%
100.0%
3 of 3 units re-run
ProvisionComputeServer
Rolled first-pass across no step: —
Steps under 20 first-time units report counts only. Full unit-level source data, every serial and release with a link to its run: 32x-production.i.etched.com/week.html#week=2026-W36

## Slide 4
What's next
two actions, each against a target and where 2026-W36 finished
a
Improve the yield / stability of L6 test
Yield target
85%
today 40.0% at MLT, 78.9% at HTT
Stability
< 10% retest
today 16.7% at MLT, 11.9% at HTT
L6 is the only level with the volume to be measured against a target at all, and it is where the line loses most of its units.
b
Speed up development of multiple L10 test units
Gate: only 1–2 units onsite
Target
3 to 10 units
assembled for test development
Coverage
full coverage
today 0 units across four steps
Not to improve the L10 yield — to make one exist. On single digits there is nothing to read, which is why every L10 box on this deck says quantity only.
The ordering is the point. Coverage, then stability, then efficiency — a station clears one gate before the next is worth measuring. L6 is at the first gate with the volume to prove it; L10 is not yet at a gate at all.

## Slide 5
Appendix — where the data comes from
every figure on this deck traces to one of these; the first one lists the units behind it
This week, unit by unit
Source data for 2026-W36 — every DUT serial, software release, verdict and a link to its run
32x-production.i.etched.com/week.html#week=2026-W36
Every week since collection began, one row each
32x-production.i.etched.com/weekly.html
The rest of the dashboard
Daily tracker — the line's own MLT/HTT tabs, rebuilt from pega3
32x-production.i.etched.com/dailyexcel.html
L10 daily tracker — FAT, SFT, RIN, 2U from pega4
32x-production.i.etched.com/l10.html
Station yield, from the controllers
32x-production.i.etched.com/direct.html
Station yield, from OCP Logs — and the measured gap between them
32x-production.i.etched.com/index.html
Run drill-down, any serial or test name
32x-production.i.etched.com/runs.html
Production test flow, with coverage
32x-production.i.etched.com/flow.html
Upstream of the dashboard
The controllers themselves — ESVM login admin / admin
pega2:3000 · pega3:3000 · pega4:3000 · pega5:3000
OCP Logs / EOS, the other side of the discrepancy
ocplogs.core.etched.com
WST and FT — Sigurd's STDF and SPLM, asked for weekly in #production-test-eng
strata6.sv9.i.etched.com:8235 · splm.i.etched.com
This deck, the pipeline that built it, and every archived week
github.com/etched-ai/factory_data_analysis · weekly/2026-W36/
All addresses are on the factory network. The dashboard rebuilds hourly; the archived copy of 2026-W36 under weekly/ does not change.