## Slide 1
32x Ramp Status (2026-W36)
2026-08-31 to 2026-09-06, week still running · first-pass yield and units, in the box · UTC
@Sigurd ASIC
ASIC
WST
32.5% reported 15d ago
FT
— reported 22d ago
SLT
at Sigurd
@Pega PCBA L6
SMT / ICT
HPB & VBB & PV1 & PDB
Flash / BFT
VBB — not in the yield view
HTT
78.9% 67u*
MLT
40.0% 90u*
ASSY
FATP L10 2U/4U
ASSY
4U
2U
FATP L10 6U
FAT / SFT
2U
ASSY
Runin
Rack L11
ASSY
FAT / SFT
Runin
counted with FAT / SFT
Pack
VBB
PV1
HPB & PDB
Green = yields, and we measure it. Amber = a yield over few units, marked *. Grey = builds, moves, or measured elsewhere.
A * marks a yield over fewer than 20 units — published, because a blank read as “nothing was tested here”, but it moves a long way on one unit. Only MLT × HTT is rolled up.
Source: pega2, pega6, pega3, pega4, pega5 (ESVM), one row per unit. WST and FT reported by Sigurd. VBB provisioning drawn for the flow but left out of the yield view.
Link: go/32x-ramp

## Slide 2
32x Rack 2
Pegatron · 2026-08-22 · assembled this week
Four Sohu servers, cabled and standing.
Rack serial 268708630001
Slot Serial
SS1 268645410001
SS2 268645440007
SS3 268645430002
SS4 268645430004
Where it stands
Assembled, not yet tested: no controller has an L11 run against this rack or its four servers. Provisioning and rack test are still ahead of it.
The all-hands page keeps this current from the controllers; this slide is a snapshot of 2026-W36.

## Slide 3
End-to-end test flow
2026-W36 · every insertion, including the ones nothing reports · grey test boxes are not collected
@Sigurd ASIC
ASIC
WST
32.5% reported 15d ago
FT
— reported 22d ago
SLT
at Sigurd
@Pega PCBA L6
BB
SMT / ICT
HPB
SMT / ICT
PV1
SMT / ICT
VBB
SMT / ICT
PDB
SMT / ICT
HTT
78.9% 67u*
MLT
40.0% 90u*
TIM
90.9% 11u*
PV1 ASSY
Flash
OTP · cert · lock BL
BFT
not collected · ETCH-39584
PDB CK
not collected
FATP L10 2U/4U
4U ASSY
2U ASSY
2U Component
counted with 2U System
FATP L10 6U
SFT
FAT
2U System
ASSY
Runin
Rack L11
ASSY
Provision
0.0% 3u*
FAT
SFT
counted with FAT
Runin
counted with FAT
Pack
Flash and BFT are two boxes, not one. Flash is the VBB provisioning we collect — ROT OTP, production certificate, bootloader lock. BFT is I2C, UART, GPIO, power-on and PRBS (ETCH-39584) and reports to no controller; drawn as one box it borrowed the provisioning yield.
2U Component and 2U System are one station key at two insertions, and FAT / SFT / Runin at L11 are one key at three — the number is printed once so the boxes cannot disagree. Source: pega2, pega6, pega3, pega4, pega5 (ESVM).